■ GU型－高真空(压力)球阀 ■ GU型高真空(压力)球阀用于接通或切断真空(压力)系统管路中的介质流。应用于真空、乳制品、酒业、生物工程、食品、制药、饮料、化妆品及化工领域。

■ GU High Vacuum(Pressure)Ball Valve ■ GU high vacuum(pressure)ball valve is used to put through or cut off the medium flow in vacuum(pressure)pipeline in the areas of vacuum, dairy products, breweries, biological engineering, foodstuff, pharmaceuticals, drinks, cosmetics and chemicals.

■ 主要技术性能 Main Technical Performance ■ ■ ■ 阀门漏率：Valve Leak Rate ≤1.3×10-4Pa.L/S. 适用温度：Applicable Temperature -30～+150℃ -30～+150℃(PPL密封) 适用范围：Appy Range 连接型式 Loose Flange 使用压力范围(Pa) 活套法兰(GB6070、JB919) 0.6×106～1.3×10-4 焊接法兰(GB6070、JB919) 1.6×106～1.3×10-4 快卸法兰(GB4982) 0.1×106～1.3×10-4 螺纹连接 Threaded Connection 1.6×106～1.3×10-4

■ 主要零件材料 Materials of Main Parts ■ ■ 阀体、阀盖、阀杆：不锈钢 密封件：四氟乙烯、丁腈橡胶、氟橡胶、PPL。 Body, disc and stem: stainless steel. Sealing element: PTFE, NBR, Viton, PPL.

CONSTRUCTION FIGHTS (mm)

■ 外形及连接尺寸(mm)(JB919) Overall and Connection Dimensions(mm)

螺纹连接的外形及连接尺寸(图一) Model 型号 DN G H E L GU-10(G) 10 1/4" 52 105 68 GU-16(G) 16 1/2" 64 130 72 GU-20(G) 20 3/4" 67 130 82 GU-25(G) 25 1" 83 165 90 GU-32(G) 32 1-1/4" 89 165 112 GU-40(G) 40 1-1/2" 100 190 120 GU-50(G) 50 2" 125 190 145 GU-63(G) 63 2-1/2" 150 250 185 GU-80(G) 80 3" 161 250 210 GU-100(G) 100 4" 180 280 268

| 活套法兰连接(GB6070)(图二) |
| --- |
|  | Model 型号 DN D Do H E L n-φc GU-10(F) 10 55 40 52 105 84 4-φ6.6 GU-16(F) 16 60 45 64 130 84 4-φ6.6 GU-25(F) 25 70 55 83 165 114 4-φ6.6 GU-32(F) 32 90 70 89 165 140 4-φ9 GU-40(F) 40 100 80 100 190 160 4-φ9 GU-50(F) 50 110 90 125 190 170 4-φ9 GU-63(F) 63 130 110 150 250 195 4-φ9 GU-80(F) 80 145 125 161 250 220 8-φ9 GU-100(F) 100 165 145 180 280 280 8-φ9 |

| 快卸法兰连接(GB4982)(图三) |
| --- |
|  | Model 型号 DN D1 D H E L GU-10(KF) 10 12.2 30 52 105 84 GU-16(KF) 16 17.2 30 64 130 84 GU-25(KF) 25 26.2 40 83 165 114 GU-32(KF) 32 34.2 55 89 165 140 GU-40(KF) 40 41.2 55 100 190 160 GU-50(KF) 50 52.2 75 125 190 170 |